## Slide 1
Multi­threaded
Optimization
by
Example
Introduction to minimizing communication barriers
(Mike Acton)

## Slide 2
Peeling Grapes with a
Sledgehammer
General­Purpose Options
•
Spinlock – Block until value can be changed.
Semaphore – Block if no remaining items
Mutex – Block if already locked
Conditional Variables – Block for event signal
Critical Section – Same as mutex. (Sometimes lighter weight.)
...and there are more
–
–
–
–
–
–

## Slide 3
The
malloc()
of
multi­threading.
We aren’t solving general­purpose
problems.
We’re solving problems specific to our games and our tech.
“Thread­safe” is a completely useless phrase in this context.
•
•
•

## Slide 4
BACKGROUND
Understand the basics for the
PPU

## Slide 5
Spinlocks
Fundamental
Hardware backed
OS Independent
•
•
•

## Slide 6
Spinlocks
LWARX (load word and reserve
STWCX (store word conditional
indexed)
indexed)
•
•
atomic_increment(
int32_t* addr )
retry:
lwarx
addi
stwcx.
r4,
r4,
r4,
0,
r4,
0,
r3
0x01 r3
;
;
;
;
Load the value. Reserve cacheline.
Increment loaded value
Try to store value.
Reservation lost, try again.
bne­ .retry

## Slide 7
The
Bad
Work on full cacheline (128 bytes)
Only one reservation per processor (i.e. A
total of ONE for us.)
•
•
The more spinlocks you use, the less effective
they are.
...and every other synchronization primitive will use some variation of them.
–
–

## Slide 8
The
Good
Relatively low overhead
Straightforward and simple
Usable in userspace
•
•
•

## Slide 9
OS­Level Synchronization Primitives
No “hard” definitions. Vary with OS.
Each are (more or less) functionally equivalent.
•
•
Imply at least wait_event
system calls.
Look at examples:
and
set_event
•
•
Mutex
Semaphore
–
–

## Slide 10
Mutex
AKA Binary Semaphore (w/ restrictions) API: Create(), Destroy(), Lock(), Unlock() Typical rules:
•
•
•
Only the locking thread can unlock
–
–
–
–
–
–
No
No
No
recursive locking
multiple unlocks multiple initialization
Thread cannot exit with open mutexes
Cannot use during interrupt callback

## Slide 11
Mutex
(Lock)
// NOTE: pthread code referenced in these slides
// been simplified somewhat to fit.
has
int pthread_mutex_lock(pthread_mutex_t *mutex)
{
// Is the mutex unlocked already?
if (atomic_exchange(&mutex­>lock, 1) != 0)
{
// Stall until we can get a lock.
while (atomic_exchange(&mutex­>lock, ­1)
{
!=
0)
//
if
Add to OS thread queue
(wait_event(mutex­>event, INFINITE)
return EINVAL;
!=
0)
}
}
return
(0);
}

## Slide 12
atomic_exchange
Simplest use of lwarx and stwcx
Returns previous value
•
•
atomic_exchange(
int32_t*
addr, int32_t value )
retry:
lwarx r0, 0, stwcx. r4, 0, bne­ .retry
r3
r3
;
;
;
;
Load the value. Reserve
Try to store value.
cacheline.
Reservation lost, try again.
Copy previous value to return
mr
r3, r0

## Slide 13
Mutex
(Unlock)
int
{
pthread_mutex_unlock(pthread_mutex_t *mutex)
idx = atomic_exchange(&mutex­>lock, 0);
// Is the mutex locked?
if (idx != 0)
{
// A lock is currently waiting for
if (idx < 0)
{
this
event.
if (set_event(mutex­>event)
return EINVAL;
<
0)
}
}
else
return EPERM;
return (0);
}

## Slide 14
Semaphore
AKA Counting Semaphore
•
•
API: Create(),
Down()
Typical rules:
Destroy(),
Get(),
Up(),
•
No owner
Can set value on creation Cannot reset value directly Cannot read value
–
–
–
–

## Slide 15
Semaphore
(Counting)
// The basis of a semaphore is being able to count
// ­1 is interpreted as ZERO
int sem_update_count(int32_t* sem_count, int incr);
.retry:
lwarx
srawi
andc
add
stwcx.
bne
mr
r0,0, r3
r1,r0,31
r1,r0,r1
r1,r1,r4
r1,0, r3
.retry
r3, r0
;
;
;
;
;
;
;
Load
the value. Reserve cacheline.
(r0 < 0)?0xffffffff:0
r0 & ~r1 (Zero if negative)
r1 + incr
r1
r1
r1
=
=
=
Try to store new value
Reservation lost, try again. Copy previous value to return

## Slide 16
Semaphore
(Basic
API)
slide.
// NOTE: Grossly over­simplified to fit
on
int sem_up( semaphore* sem )
{
sem_update_count( &sem­>count,
set_event( &sem­>event );
return (0);
}
+1 );
int sem_down( semaphore* sem )
{
// Wait until an item is available
while ( sem_update_count( sem_count,
{
wait_event( &sem­>event );
}
return (0);
}
­1
) == 0
)

## Slide 17
Typical
Example
Fixed size buffer of objects (queue)
Thread­1 (Producer)
•
•
Adds objects to queue
available.
Thread­2 (Consumer)
so long as space
is
–
•
Removes (processes) objects from queue so
long as there are objects remaining.
–

## Slide 18
Example
(1)
Producer
Init:
mutex_init( &full_of_ideas, LOCKED )
mutex_init( &out_of_ideas, LOCKED )
while (1)
{
if ( queue_is_full( &idea_queue ) )
{
mutex_unlock( &full_of_ideas );
mutex_lock( &out_of_ideas );
}
idea = make_idea(); mutex_lock(
&idea_key ); queue_push(
&idea_queue, idea );
mutex_unlock( &idea_key );
}

## Slide 19
Example
(1)
Consumer
while (1)
{
mutex_lock( &full_of_ideas );
mutex_lock( &idea_key );
while ( queue_is_not_empty( &idea_queue
{
idea = queue_pop( &idea_queue );
take_advantage_of( &idea );
}
mutex_unlock( &idea_key );
)
)
mutex_unlock( &out_of_ideas );
}

## Slide 20
Example
(2)
Producer
Init:
semaphore_init(
semaphore_init(
semaphore_init(
&ideas_made,
&ideas_used,
&idea_key,
QUEUE_SIZE
0 );
1 );
);
while (1)
{
semaphore_down(
&ideas_made );
idea = make_idea();
semaphore_down( &idea_key );
queue_push( &idea_queue, idea );
semaphore_up( &idea_key );
semaphore_up( &ideas_used );
}

## Slide 21
Example
(2)
Consumer
while (1)
{
semaphore_down( &ideas_used );
semaphore_down( &idea_key );
idea = queue_pop( &idea_queue );
semaphore_up( &idea_key );
take_advantage_of( &idea );
semaphore_up( &ideas_made );
}

## Slide 22
End
of
background
section
Now let's talk about where it can
be done better.

## Slide 23
REAL
EXAMPLE
Look at the actual queue used by
the TcpServer example (later)

## Slide 24
Atomic
Read/Write
Unfortunately “atomic” has been too
heavily overloaded to use meaningfully.
Typically, at a high level: “Atomic” means both indivisible and guaranteed. e.g. spinlock atomic_increment().
•
•
But it also simply means indivisible. i.e.
will either succeed or not, but never partially.
It
•

## Slide 25
Atomic
Functions
//
//
//
//
These functions must not be inlined on the x86. In order to ensure that the writes and reads are atomic, the compiler must not be given
any opportunity to fold the operation into a more complex instruction
e.g.
load­increment­store
void void uint32_t
AtomicWrite32Aligned( uintptr_t address, uint32_t arg ); AtomicWritePointerAligned( uintptr_t address, uintptr_t arg ); AtomicRead32Aligned( uintptr_t address );
Why is the x86 different from the PPC here?
•

## Slide 26
Side­Topic
(Validation)
What if a read or write needs to be atomic but it wasn’t?
•
Multi­threaded programming and optimization are by­contract (mutual agreement)
Similar to data (parameter) contracts to functions, but…
There is often no way to meaningfully validate correctness (assert).
Be thorough. Test. Talk it through with someone.
–
–
–
–

## Slide 27
Atomic
Functions
void
AtomicWrite32Aligned(
{
// Aligned 32 bit
// Aligned 32 bit
uintptr_t address, uint32_t
arg )
writes writes
are always atomic are always atomic
on on
x86
PowerPC
assert( (address & 0x03)
== 0 );
uint32_t* p = (uint32_t*)address;
*p = arg;
}
Could this, in fact, be inlined?
•
Yes – with inline assembly
to select the
proper
instruction.
•
BUT LOOK OUT!
•
Peephole optimizations
Link­level optimizations
•
•

## Slide 28
Atomic
Functions
void
AtomicWritePointerAligned( uintptr_t address, uintptr_t arg )
{
//
//
Aligned
Aligned
32
32
bit bit
writes writes
are are
always atomic on x86 always atomic on PowerPC
//
//
Aligned
64
bit
writes
are
not always atomic on x86,
so
if
pointers are 64 bits,
this needs to be re­written.
assert( (address & 0x03)
== 0 );
uintptr_t* p = (uintptr_t*)address;
*p = arg;
}

## Slide 29
Atomic
Functions
uint32_t
AtomicRead32Aligned( uintptr_t address
{
)
// Aligned 32 bit reads are
// Aligned 32 bit reads are
always always
atomic on x86 atomic on PowerPC
assert( (address & 0x03) ==
0 );
volatile uint32_t* p = (uint32_t*)address;
return (*p);
}
NOTE: Use of volatile is not strictly necessary
•
here. There is no way for this read to get folded
out.
On the PPC this same function could be inlined
•
and the volatile would be necessary.

## Slide 30
Fixed Queue
Example
Some things are knowable
theoretical exersize:
–
this
isn’t
a
•
Very Common Case:
–
Single Reader (Consumer)
Single Writer (Producer)
•
•
Plan the data access patterns.
–
Multithreading is much easier for
write­only cases.
Use read­write carefully.
read­only and
•
•

## Slide 31
Fixed
Queue
Example
Single­Reader, Single­Writer
Fixed­Sized Lookaside Dequeue
Rules for use:
Push() can only be called from one thread,
but it
•
doesn't need to be the same thread as Pop().
Pop() can only be called from one thread, but it
doesn't need to be the same thread as Push().
max_count must be a power of two. Don't Pop() more than Count()
Check IsFull() or Count() before a Push()
•
•
•
•

## Slide 32
SrSwFixedLookasideDequeue
struct SrSwFixedLookasideDequeue
{
// DO NOT uint32_t uint32_t uint32_t
MODIFY DIRECTLY m_pushed_count; m_popped_count; m_max_count;
// API void uint32_t int uint32_t void uint32_t void
Clear( uint32_t Count(); IsFull();
max_count
);
NextPushElement(); Push(); NextPopElement(); Pop();
};

## Slide 33
SrSwFixedLookasideDequeue
inline void
SrSwFixedLookasideDequeue::Clear( uint32_t
{
max_count )
//
//
//
//
//
//
//
These writes don't need to be atomic.
The assumption is that either:
(1)
This is only (i.e. init), If the queue
done once before or
the queue is actually used
(2)
is going to be cleared there will certainly be some
need to synchronize at a higher level, so pointless to do it here too.
m_pushed_count m_popped_count m_max_count
=
=
=
0;
0;
max_count;
}

## Slide 34
SrSwFixedLookasideDequeue
// Get Number of items in the queue
inline uint32_t
SrSwFixedLookasideDequeue::Count()
{
uintptr_t uintptr_t uint32_t uint32_t uint32_t
pushed_count_addr popped_count_addr pushed_count popped_count
diff
=
=
=
=
=
(uintptr_t)&m_pushed_count; (uintptr_t)&m_popped_count; AtomicRead32Aligned( pushed_count_addr AtomicRead32Aligned( popped_count_addr pushed_count ­ popped_count;
);
);
return (diff);
}
These reads will be
complete (atomic) but not necessarily
•
most­recent. (This is not a problem.)
NOTE: Because counts are unsigned, overflow is not a
•
problem.
e.g. in 8 bits: 0x01 (1) – 0xfe (254) = 0x03 (3)
•

## Slide 35
SrSwFixedLookasideDequeue
// Check if the queue is full.
inline int
SrSwFixedLookasideDequeue::IsFull()
{
uint32_t element_count = Count();
return (element_count == m_max_count);
}

## Slide 36
SrSwFixedLookasideDequeue
With SrSw it doesn’t matter if Count() changes while or
•
immediately after IsFull() is called:
If
IsFull() is used to determine if there is space –
•
it is the thread that does the Push() that makes this
call
•
so…
it cannot be made more full by another thread,
only more empty.
•
•
If
IsFull() is called by the Pop()’ing thread (Consumer)
•
(If TRUE) Only this thread can make it less full, so it is
•
necessarily true.
(If FALSE) If can be made full immediately after, and
•
the check can be missed – but since this can only be
conceivably used for polling – it will be hit the next time around.

## Slide 37
SrSwFixedLookasideDequeue
// Return the index of the next element that would be pushed.
inline uint32_t
SrSwFixedLookasideDequeue::NextPushElement()
{
uintptr_t uint32_t uint32_t
pushed_count_addr pushed_count element_ndx
=
=
=
(uintptr_t)&m_pushed_count; AtomicRead32Aligned( pushed_count_addr pushed_count & ( m_max_count ­ 1 );
);
return (element_ndx);
}
This function can only
be called from the Push()’ing thread
•
(Producer)
The count read is always the complete (atomic) and the most
•
recent (only this thread can change it.)
element_ndx = pushed_count % m_max_count;
•

## Slide 38
SrSwFixedLookasideDequeue
inline void
SrSwFixedLookasideDequeue::Push()
{
uintptr_t pushed_count_addr = (uintptr_t)&m_pushed_count;
uint32_t
pushed_count
= AtomicRead32Aligned( pushed_count_addr ) +
1;
AtomicWrite32Aligned( pushed_count_addr, pushed_count );
}
The incremement itself does not need to be atomic since only
•
a single thread can write to this address.
But the write must be atomic since multiple threads can read.
•

## Slide 39
SrSwFixedLookasideDequeue
// Return the index of the next element that would be popped.
inline uint32_t
SrSwFixedLookasideDequeue::NextPopElement()
{
uintptr_t uint32_t uint32_t
popped_count_addr popped_count element_ndx
=
=
=
(uintptr_t)&m_popped_count; AtomicRead32Aligned( popped_count_addr popped_count & ( m_max_count ­ 1 );
);
return (element_ndx);
}
Pretty much the same
This function can only
as
be
NextPushElement()
called from the Pop()’ing thread
•
•
(Consumer)
The count read is always
the complete (atomic) and the
•
most recent (only this thread can change it.)
element_ndx = popped_count % m_max_count;
•

## Slide 40
SrSwFixedLookasideDequeue
inline void
SrSwFixedLookasideDequeue::Pop()
{
uintptr_t popped_count_addr = (uintptr_t)&m_popped_count;
uint32_t
popped_count
= AtomicRead32Aligned( popped_count_addr ) +
1;
AtomicWrite32Aligned( popped_count_addr, popped_count );
}
Pretty much the same as Push()
The incremement itself does not need to be atomic since
•
•
only a single thread can write to this address.
But the write must be atomic since multiple threads can
•
read.

## Slide 41
SrSwFixedLookasideDequeue
That’s it.
•
This is now a very simple, very fast queue that can be used in
•
a multithreaded environment.

## Slide 42
Example
(3)
Producer
Init:
Idea idea_buffer[ QUEUE_SIZE ]; // QUEUE_SIZE=power
SwSrFixedLookasideDequeue idea_queue;
idea_queue.Clear( QUEUE_SIZE );
of
two
while (1)
{
if ( idea_queue.IsFull()
{
// Sleep, stall, fail
}
)
or do some other work.
uint32_t next_idea_ndx =
idea_queue.NextPushElement();
make_idea();
Idea
idea
=
idea_buffer[ next_idea_ndx ] = idea;
AtomicStoreFence();
idea_queue.Push();
}
Note that the buffer is written to before the push is done. If it is
not done in this
•
order, there is a race condition.
If there is a store reorder buffer on the processor, a store fence must be used to
•
guarantee the order.

## Slide 43
Atomic
Load/Store
Fence
//
//
These fences are only needed on architectures
that
have load­store re­ordering
These only apply to access
of system memory
//
Pentium
#define AtomicStoreFence()
#define AtomicLoadFence()
asm { sfence }
asm { lfence }
// PowerPC
#define AtomicStoreFence()
#define AtomicLoadFence()
asm { lwsync }
asm { lwsync }
// But on the PPU
#define AtomicStoreFence()
#define AtomicLoadFence()
For system memory
accesses –
•
StoreFence: Ensure that all previous
stores will be
•
completed before any following stores.
LoadFence: ensure that all previous loads will be
•
completed before any following loads.

## Slide 44
PowerPC
Sync
For PowerPC, sometimes you will see { sync }
•
This is a “heavy­weight” sync – All load/store
•
instructions before the sync will be completed before
instructions following.
any
Including instructions across:
•
System memory
Cache inhibited (uncached memory)
Gaurded (I/O mapped device memory e.g. SPU
•
•
•
addresses, etc.)
For PowerPC, sometimes you will see { eieio }
•
Enforce In­Order Execution of I/O
This is basically the same as a { sync } enforces the
•
•
order within each type of memory, not across all types.

## Slide 45
Example
(3)
Producer
while (1)
{
if ( idea_queue.IsFull() )
{
// Sleep, stall, fail or do some other work.
}
. . .
Where you would normally see a Sleep() in a standalone
•
server, in the context of a game we have both a main loop
a vsync – natural places to “restart” background tasks.
and
The frame can also be split into multiple sub­frames
that
•
trigger (and spread) the load across the game cycle.
if ( idea_queue.IsFull() )
{
return; // Will add it next time around.
}
. . .

## Slide 46
Example
(3) Consumer
uint32_t idea_count
while (idea_count)
{
uint32_t idea_ndx
=
idea_queue.Count();
=
=
idea_queue.NextPopElement();
idea_buffer[ idea_ndx ];
Idea
idea
AtomicLoadFence();
idea_queue.Pop();
idea_count­­;
}

In the same way as the Producer, the
data must
be taken from the buffer before it is Pop()’d or there
will be a race condition.

## Slide 47
TCP
SERVER
Putting some of this together
toward a faster TCP server.

## Slide 48
TcpServer
Concept:
(1)
Be pretty close to the design ideas of the pre­
existing
(2)
one in IPC
No standard sync primitives (e.g. compare­swap,
critical­section, etc.)
i.e. completely lock­free.
(3)
Support multiple client connections.

## Slide 49
TcpServer
TCPSERVER_MAX_CONNECTIONS 256
#define
#define
TCPSERVER_QUEUE_LENGTH
64
typedef typedef
void* (TcpServerAllocFunc)
( size_t size );
void
(TcpServerFreeFunc)
( void* ptr
);
// (1)
// (2)
A TcpServer must be aligned
on a 32 bit boundary
A TcpServer can only be owned by a single user thread.
struct
{
TcpServer

## Slide 50
TcpServer
NO DATA SHOULD BE MODIFIED DIRECTLY
//
//
//
//
//
This data is only modifiable from the server thread. Non­atomic access is acceptable. This data may not be accessed by the user thread.
IPC::TcpConnection uint16_t
uint16_t Socket ThreadHandle int
m_connection;
m_server_port;
_pad_0; m_server_socket; m_server_thread; m_server_thread_running;
Socket uint32_t uint32_t
m_client_connection_table [TCPSERVER_MAX_CONNECTIONS];
m_client_addr_table
[TCPSERVER_MAX_CONNECTIONS];
m_client_connection_end_count;
Everything is
32 bit aligned.
Need to know the size of all the types.
This is made more difficult with extra opaque typing layers.
sizeof(Socket) sizeof(ThreadHandle) sizeof(ThreadHandle)
==
==
==
sizeof(int)
sizeof(HANDLE)
== sizeof(void*)
// WIN32
sizeof(sys_ppu_thread_t) == sizeof(uint64_t) // PPU

## Slide 51
TcpServer
is only read­write from the server thread. This data is is
// This data
// read­only
from
the
user
thread. Reads and writes must be atomic.
int32_t int32_t
m_server_thread_errno;
m_server_thread_errln;
Note with multithreaded design, there must be very clear rules for how data is
accessed.
Otherwise, everything will get out of control and non­optimizable. (Remember
malloc()!)

## Slide 52
TcpServer
The inbound message dequeue is read­write from the server thread and read­only from the user thread. Atomic access is handled by SrSwFixedLoookasideDequeue.
//
//
//
SrSwFixedLookasideDequeue
m_inbound_message_dequeue;
//
//
//
The outbound message dequeue is read­write from the user thread and read­only from the server thread. Atomic access is handled by SrSwFixedLoookasideDequeue.
SrSwFixedLookasideDequeue
m_outbound_message_dequeue;
TcpServerMessage* TcpServerMessage*
m_inbound_messages [ TCPSERVER_QUEUE_LENGTH
m_outbound_messages [ TCPSERVER_QUEUE_LENGTH
];
];
Note that separate queues
read data and written data.
are
used. This is based on the principle of separating
This makes things much easier. (And faster)
This principle does not just apply to multithreading, either!

## Slide 53
TcpServer
These functions are callable from either thread, but can only be once in initialization. The memory manager must be atomic across
//
//
//
//
written
multiple threads another.
because ownership is shifted from one thread to
TcpServerAllocFunc* TcpServerFreeFunc*
m_call_alloc;
m_call_free;
Allocating messages was
in the original design.
Assumption: There is some fast method of allocating messages in the calling
context. e.g. a fixed pool of messages.
Assumption: This may be used in different contexts within the same application –
so may need different alloc/free routines. So, not using static members.

## Slide 54
TcpServer
(Called from user thread)
//
// PUBLIC
//
API
int
Start( uint16_t port, TcpServerAllocFunc* TcpServerFreeFunc*
WaitForClose(); Kill(); GetErrno(); GetErrln();
alloc,
free
);
void void int32_t int32_t
TcpServerMessage*
CreateMessage( uint32_t uint32_t uint32_t uint32_t
tag, uint32_t size, transaction, client_ndx, client_addr );
void uint32_t uint32_t void
int
DestroyMessage( TcpServerMessage* message ); CountInboundMessages(); CountOutboundMessages();
PopInboundMessage( TcpServerMessage** message_result
PushOutboundMessage( TcpServerMessage* message );
);
Taking a message from the system implies you take ownership of the data.
Giving a message to the system implied you give away ownership of the data.

## Slide 55
TcpServer
(Called from server thread)
//
// INTERNAL
//
void int void int int void
SetError( int32_t thread_errno, int32_t thread_errln );
PushInboundMessage( PopOutboundMessage( AcceptNewClient(); HandleIncomingData(
TcpServerMessage* message ); TcpServerMessage** message_result
);
fd_set* server_read_fd );
HandleOutgoingData();
int
ReadSocketData( uint32_t client_ndx, char* buffer, uint32_t buffer_size );
int
WriteSocketData( uint32_t client_ndx, char* buffer, uint32_t buffer_size );
void
CloseClientConnection( uint32_t client_ndx );
};

## Slide 56
EchoServer
First, look at EchoServer.cpp of how this is used.
for example
•
Then, look at the interesting parts of
TcpServer.cpp
•

## Slide 57
TcpServer (Internal)
void
TcpServer::SetError( int32_t thread_errno, int32_t thread_errln )
{
uintptr_t thread_errno_addr = (uintptr_t)&m_server_thread_errno;
uintptr_t thread_errln_addr = (uintptr_t)&m_server_thread_errln;
// The write order is
// that when errno !=
important. errln must be written first, so
0 is read, errln is gauranteed to be ready.
AtomicWrite32Aligned( AtomicStoreFence(); AtomicWrite32Aligned(
thread_errln_addr, (uint32_t)thread_errln );
thread_errno_addr, (uint32_t)thread_errno );
}
An error is made up of two parts – the errno and the line it occurred on.
We must ensure that they are read together.
This principle does not just apply to multithreading, either!

## Slide 58
TcpServer
(Internal)
void
TcpServer::PopInboundMessage( TcpServerMessage** message_result )
{
uint32_t message_ndx = m_inbound_message_dequeue.NextPopElement();
//
//
//
The (1) (2)
read from the write the value
m_inbound_messages does not need to be atomic since was gauranteed to be complete (i.e. was atomic) and,
cannot be over­written until the
Pop() is complete.
*message_result = m_inbound_messages[ message_ndx
];
//
//
//
//
But it is important that the pop be done after
the pointer is read
i.e. ownership has been given to the user thread, because once the
pop is complete it may be immediately overwritten by the server thread. Doing the pop before reading the pointer would cause a race condition.
AtomicLoadFence();
m_inbound_message_dequeue.Pop();
}
Pretty much the same as the Consumer example.
But note the non­atomic read.

## Slide 59
TcpServer
(Internal)
int
TcpServer::PushOutboundMessage( TcpServerMessage* outbound_message
{
if ( m_outbound_message_dequeue.IsFull() )
{
return (0);
}
)
uint32_t
message_ndx
=
m_outbound_message_dequeue.NextPushElement();
TcpServerMessage** outbound_message_ind =
&m_outbound_messages[ message_ndx ];
AtomicWritePointerAligned( (uintptr_t)outbound_message_ind, (uintptr_t)outbound_message );
AtomicStoreFence();
m_outbound_message_dequeue.Push();
return (1);
}
Pretty much the same as the Producer example.
But note atomic write of the pointer, which will be required by the pop.

## Slide 60
TcpServer
(Internal)
HandleOutgoingData() processes all the
pending messages sends them to the appropriate clients.
void
TcpServer::HandleOutgoingData()
{
uint32_t outbound_message_count = CountOutboundMessages();
•
while ( outbound_message_count )
{
Note, the count is only read once. The server only empties out the part of
the queue it knows about at the start.
New messages may be added while these are being processed, no problem.
They will just be processed next time around.
•
•
•

## Slide 61
TcpServer
(Internal)
TcpServerMessage*
h_outbound_message;
TcpClientMessageHeader n_outbound_message_header;
PopOutboundMessage( &h_outbound_message );
int32_t int32_t
message_client_ndx message_client_addr
= h_outbound_message­>m_header.m_client_ndx;
= h_outbound_message­>m_header.m_client_addr;
Socket
client_socket
= m_client_connection_table[ message_client_ndx
= m_client_addr_table[ message_client_ndx ];
];
uint32_t client_addr
if (
{
//
//
client_socket == m_server_socket )
This connection has been dropped. There's no where for this message to go. Drop message.
goto CLEANUP_OUTBOUND_MESSAGE;
}
if (
{
//
//
client_addr != message_client_addr )
This connection has been dropped and since re­opened with a new client. Drop message.
goto CLEANUP_OUTBOUND_MESSAGE;
}
Note Client and Server Message headers are different
•
– Server stores more information.
Match the message to a client.
•

## Slide 62
TcpServer (Internal)
// Gather outbound message
(client)
header information in host format.
uint32_t uint32_t uint32_t
h_message_tag h_message_size h_message_transaction
=
=
=
h_outbound_message­>m_header.m_tag; h_outbound_message­>m_header.m_size; h_outbound_message­>m_header.m_transaction;
// Convert to network format
(big­endian)
uint32_t uint32_t uint32_t
n_message_tag n_message_size n_message_transaction
=
=
=
htonl( htonl( htonl(
h_message_tag ); h_message_size ); h_message_transaction
);
// Create outbound client header
in
network format
n_outbound_message_header.m_tag n_outbound_message_header.m_size n_outbound_message_header.m_transaction
=
=
=
n_message_tag; n_message_size; n_message_transaction;
// Gather outbound message data
char*
message_data
= h_outbound_message­>m_data;
There are standard functions for network<­>host translation.
Network byte order at the transport layer is BIG ENDIAN.
We can also say the PPU is a NETWORK BYTE ORDER machine.
i.e. If you assume the code will only run on a big­endian machine, you can
•
•
•
•
assume it will only run with network byte order.

## Slide 63
TcpServer
(Internal)
int write_header_valid = WriteSocketData( message_client_ndx, (char*)&n_outbound_message_header,
sizeof(TcpClientMessageHeader) );
if (!write_header_valid)
{
// Drop message.
goto CLEANUP_OUTBOUND_MESSAGE;
}
int write_data_valid =
WriteSocketData(
message_client_ndx, message_data, h_message_size );
if
{
(!write_data_valid)
Push data over socket.
If write fails, we’ve lost the
•
•
// Drop message.
goto
CLEANUP_OUTBOUND_MESSAGE;
connection – just drop the packet.
}
When the client re­connects, they
•
CLEANUP_OUTBOUND_MESSAGE:
will need to re­sync anyway.
m_call_free( h_outbound_message­>m_data m_call_free( h_outbound_message );
);
outbound_message_count­­;
}

## Slide 64
EchoServer
OK. Anything more interesting than this not going to fit on these slides.
is
•
We probably have about 15­20 minutes left – let’s open up TcpServer.cpp and walk through it.
(?)
•
But at this point you have the main concepts that are used.
•